## Slide 1
Date: 22/03/2018
Place: DTU, Denmark
Enea Mustafaraj, PhD
Epoka University
Tirana, Albania
Knowledge FOr Resilient soCiEty
BOMB CALORIMETER EXPERIMENT PRESENTATION
The European Commission support for the production of this publication does not constitute an endorsement of the contents which reflects the views only of the authors, and the Commission cannot be held responsible for any use which may be made of the information contained therein.

## Slide 2
ABSTRACT
In this report it is presented the the bomb calorimeter test on two materials; oat and creamer. The heat of combustion was measured by using 1 gram of each material. The data were then compared with previous experiments.
The experiment took place in Fire Lab in Building 122 of DTU.

## Slide 3
INTRODUCTION
Knowledge of the Calorific value of the materials is a good indicator in determining of how the fire will behave.
I.e. A material with high caloric value,
  would contribute to a long duration fire,
  would produce more heat
  would create a more difficult fire to extinguish.

## Slide 4
INTRODUCTION – (terms and definitions)
Calorimetry is the science of measuring quantities of heat. The instruments used for such measurements are known as calorimeters.
Oxygen bomb calorimeters, are the standard instruments for measuring calorific values of solid and liquid combustible samples.
The calorific value (heat of combustion): the number of heat units liberated by a unit mass of a sample when burned with oxygen in an enclosure of constant volume.
  (the heat liberated by the combustion of all carbon and hydrogen with oxygen to form carbon dioxide and water, including the heat liberated by the oxidation of other elements present in the sample).

## Slide 5
The units of the heat energy are :
  calories (cal),
  British thermal units (Btu) or
  Joules (J)
1 calorie = 4.1868 absolute Joules, and is roughly equivalent to the heat energy required to raise the temperature of one gram of water one degree Celsius at 15°C.
The British thermal unit equals 251.996 calories and is roughly equivalent to the heat energy required to raise one pound of water one degree Fahrenheit at 60°F.
INTRODUCTION – (units & unit conversion)

## Slide 6
INTRODUCTION
In this report it is presented the the bomb calorimeter test on two materials; oat and creamer. The heat of combustion was measured by using 1 gram of each material.
Figure 1. Substances to be tested.

## Slide 7
METHODOLOGY
thermometer
bomb
1 g substance
water at 20℃
The bomb containing 1 gram of any substance is placed inside the calorimeter which then is filled with water.
The substance will be ignited using a cotton wire and the temperature difference of the water can be measured by a thermometer.
In order to have a complete combustion, the bomb is filled with pressurized oxygen gas at 30 atm.
Figure 2. Calorimeter bomb scheme (Parr, 2007)

## Slide 8
METHODOLOGY – effective heat of combustion
where:
C : calibration value for the system (10070 J/K)
q’wire : the energy content in the wire (50 J per cotton wire)
m : mass of the sample [kg]
∆T : the temperature change in the system
(Equation 1)

## Slide 9
METHODOLOGY – Procedure of application
Figure 3. a) equipment needed for experiment, b) weighting of 1 gram of substance, c) preparation of the hook.

## Slide 10
Figure 4. a) preparation of hook and crucible, b) mounting of the bomb, c) inserting pressurized oxygen at 30 atm.
METHODOLOGY – Procedure of application

## Slide 11
Figure 5. a) fixing of the bomb inside calorimeter, b) filling the calorimeter with 2 L of water, c) starting the program.
METHODOLOGY – Procedure of application

## Slide 12
RESULTS AND DISCUSSION
Figure 6. Output results for both substances

## Slide 13
After the experiment, the results were compared with the standard values given on the table (http://webbook.nist.gov)
RESULTS AND DISCUSSION
 | Experimental results | Table values | Deviation
Oat | 17470 J/g | 14895 J/g | 17,28%
Creamer | 22300 J/g | 20752 J/g | 7,46%
Table 1. Experimental vs. table results for oat and creamer.

## Slide 14
As it can be seen from Table 1, oat has the highest variability of 17,28%. This result can be explained with the heterogeneous nature of oat seeds.
The creamer on the other hand, seems to have a smaller variance. It can be explained with the more controlled environment where the dust is produced.
RESULTS AND DISCUSSION

## Slide 15
RESULTS AND DISCUSSION – other substances
 | Experimental results (J/g) | Table values (J/g) | Deviation
Sugar | 16636 | 16488 | 1%
Heptane | 47422 | 48170 | 2%
Dodecane | 47886 | 47547 | 1%
Flour | 16381 | 18354 | 11%
Benzoic | 26040 | 26451 | 2%
Oat | 17552 | 14895 | 18%
Creamer | 21658 | 20752 | 4%
Toluene | 42558 | 42609 | 0%
Table 2. Other experimental results for various substances

## Slide 16
RESULTS AND DISCUSSION – other substances
Figure 6. Comparison of heat of combustion data for various substances

## Slide 17
CONCLUSIONS
In this report it is presented the the bomb calorimeter test on two materials; oat and creamer. The results were compared with previous experiments done at DTU.
As expected, oat had a smaller heat of combustion value when compared to creamer.
This test could also be useful to compare the calorific values of various food substances used in human bodies as the amount of heat needed to burn in the bomb calorimeter is the same as the energy released when human body burns them.

## Slide 18
References
http://webbook.nist.gov
http://www.scimed.co.uk/wp-content/uploads/2013/03/Introduction-to-bomb-calorimetry.pdf
Fire Dynamics reports, DTU, 2017

## Slide 19
Thank you
emustafaraj@epoka.edu.al
Knowledge FOr Resilient soCiEty